## Slide 1
Design with the knowledge base and arch2code
The integrated flow for Lattice FPGA system design: start from what the team knows, leave behind what the next design needs
flow
For design and verification engineers | FPGA design tools, October 2026
Notes: Opening. The one sentence to leave with: a design starts from what the team already knows and leaves behind what the next design needs. This deck is for engineers who will run the flow and contribute entries. Every claim is backed by something that exists in the repositories today, so any slide can be shown live.

## Slide 2
Today, every design re-derives what the last one already knew
Design with the knowledge base and arch2code
2
Where knowledge lives today
What the flow changes
1
In people's heads
The register map of the last SoC, the PLL settings that worked, the pin that was swapped on the board: known by one engineer.
2
In old projects nobody reopens
Constraints, IP configurations and flow results sit in archived Radiant projects without a summary.
3
Re-derived every time
A new design repeats the same investigation of IP catalog records, board facts and address maps.
4
The AI agent answers from memory
Without evidence the agent guesses offsets, versions and parameters, and the guess looks confident.
1
Captured once, cited every time
Hierarchy, constraints, IP usage, flow results and registers of every captured design, each value with its file and line.
2
Searched before anything is built
The flow starts with a knowledge search; reuse is proposed with evidence, rejections are recorded with reasons.
3
Recorded as it runs
Intent, decomposition, decisions and hand-off are files, so a session or a colleague can continue from them.
4
Enriched by using it
Capture is the last stage of every design; derived knowledge refreshes itself from the repositories.
Notes: Left: the situation most teams are in. Right: what changes with the flow. The point is not that engineers lack knowledge; it is that the knowledge is not in a place a tool, or a new colleague, can read. The agent in particular answers from its training memory unless it is given evidence, and memory is where wrong register offsets and stale IP parameters come from.

## Slide 3
Five phases, thirteen stages, three human gates
Design with the knowledge base and arch2code
3
A Intake
1 intake
2 intent record
3 knowledge search
B Architecture
4 decomposition
5 YAML and skeleton
6 model simulation
C Realisation
7 SoC session
8 RTL and register test
9 constraints
D Build, bring-up
10 Radiant build
11 firmware
12 programming, smoke test
E Hand-off
13 hand-off and capture
Gate 1 intent
Gate 2 decomposition
Gate 3 implementation review
After Gate 2 the agent does not stop for a question until Gate 3: it records every assumption and every fix in design/decisions.md and reports them. A design that already exists enters at the stage its mode gives (extend an arch2code project, vary a captured design, extend a Propel SoC, debug) with a delta intent record instead of a new one.
Notes: Walk the chevrons left to right. Phases A and B are the design-from-intent flow in arch2code: intake, knowledge search, decomposition, YAML, model simulation. Phase C realises the design: the SoC branch through Propel, RTL, constraints. Phase D builds the bitstream, the firmware and brings the board up. Phase E hands off and captures. The three gates are the only places the engineer must approve: the intent, the decomposition, and the implementation review before the Radiant build. After Gate 2 the agent records assumptions instead of asking.

## Slide 4
What the engineer does, what the agent does
Design with the knowledge base and arch2code
4
Engineer
Agent
1
Answers the intake
function, interfaces, performance, software view, reuse, device, verification, end point, environment
2
Approves the gates
intent, decomposition with the SoC and implementation tables, implementation review
3
Answers governance
maturity, license, provenance, export control, classification, once, at capture
4
Holds the hardware
board, cable, smoke test observation
1
Searches
designs, modules, patterns, IP, boards, skills; rejections recorded
2
Generates
decomposition, YAML, skeletons, stubs, models, headers, documentation
3
Simulates, builds
model, co-simulation, register-access test, Propel session, Radiant, firmware
4
Records
assumptions, fixes, derivations, open items, hand-off, capture
Notes: Two lanes. The engineer's time is spent where judgement matters: the intake answers, the three gates, the governance answers at capture, and the hardware. The agent's time is spent searching, proposing, generating, simulating, building and writing the records. The rule after Gate 2 keeps the engineer out of the loop for routine decisions, every one of which is written down.

## Slide 5
Six records make the flow restartable
Design with the knowledge base and arch2code
5
1
intent.yaml
The intake answers, assumptions and open questions; frozen at Gate 1. A delta record for an existing design.
2
decomposition.md
Blocks, origins, interfaces, the implementation plan table and, on the SoC branch, the SoC table.
3
decisions.md
Append-only log: every candidate selected or rejected with its reason, every gate, assumption, fix, derivation and open item.
4
ip-bindings.yaml
The IP cores and versions bound to the design, the donor design and its capture commit.
5
gaps.yaml
Facts the knowledge base and the servers could not supply, with the source the engineer used instead.
6
handoff.md
Entry mode, approvals, block table, bindings, what simulation proved, derived registers, stages not yet run, risks.
A new session starts from these files, not from memory
Notes: These files live under design/ in the project and are deliverables, not notes. They are written as the flow runs, never reconstructed from memory afterwards. The hand-off record is what the implement-from-handoff skill starts from, in the same session or a later one, on the same machine or another. The gap log is where every fact the knowledge base could not supply is recorded, which is how the knowledge base learns what it is missing.

## Slide 6
Four servers behind one agent, and who answers what
Design with the knowledge base and arch2code
6
Claude Code
with the skills
a2c
arch2code
Database, scaffold, generate, model build and run, co-simulation, regression, register-access test, Questa lint.
kb
cortex-kb
Designs, modules, patterns, IP catalog, boards, device notes, skills, registers; authoring tools in your own session.
soc
lattice-cortex
Propel IP facts and compatibility, the SoC session and its equivalence checks, replay and comparison of the arch2code SoC manifest, DGE and SGE, firmware plan and tests.
rad
lattice-radiant-mcp
Radiant project, synthesis to bitstream, timing closure levers, constraints lint, programming, Reveal debug. Own installer, registered beside the bundle.
bundle
bundle
bundle
Precedence: a fact is taken from the server that owns it (IP facts from lattice-cortex, device facts from the Radiant server, verified designs from cortex-kb, the project's own YAML from arch2code); a conflict is recorded, never averaged.
Notes: The agent in Claude Code talks to four MCP servers registered side by side. Three come out of the lattice-prompt bundle and are registered by its installer: arch2code owns generation and simulation of the project; cortex-kb owns evidence, what exists, what was verified, where a value comes from; lattice-cortex owns the Propel SoC session, the IP facts and the firmware, and since release 0.2.0 the replay of an arch2code SoC manifest. The Radiant server ships with its own installer and owns the build, timing closure, programming and Reveal debug. When two servers know the same fact, the precedence rule in the project's AGENTS.md says which one wins and the disagreement is recorded.

## Slide 7
Eight kinds of entry, three ways a design gets in
Design with the knowledge base and arch2code
7
D
Designs
Whole verified designs with hierarchy, flow results, constraints, IP usage, registers and history
M
Reusable modules
Modules marked reusable, with ports, parameters and the designs that instantiate them
P
Patterns
Idioms that worked (CDC, reset, handshake) and anti-patterns to check against
I
Interfaces
Bus and stream protocol definitions shared across entries
IP
IP catalog
Core records with versions, parameters, ports, bus interfaces, register maps and family support
B
Boards
Pin sites, reference clocks, bank voltages; JTAG and programming facts as they are added
N
Device notes
Family-specific facts and the style guide the agent must follow
S
Design skills
Procedures for changing a design, reviewed and installable into Claude Code
linked
the upstream Git repository is pinned; rescans follow it
vendored
a copy is taken once when no repository exists; tree hash recorded
knowledge-only
derived facts only; sources stay where they are and are never copied
Notes: The knowledge base is a Git repository of entries plus a session database built from it. Designs are the heavyweight entries; modules and patterns are what gets reused most; IP catalog records are synced from the IP server; boards and device notes hold the facts that are usually in someone's notebook; skills are recorded procedures. A design is linked to its upstream repository, vendored when there is no repository, or knowledge-only when the sources must not enter the knowledge base at all.

## Slide 8
Anatomy of a design entry: cpnx_gsrd
Design with the knowledge base and arch2code
8
Hierarchy
modules, instances, lines
Ports and parameters
of the top and every module
Constraints
clocks, generated clocks, I/O
IP usage
cores, versions, parameters
Flow results
resources, timing, warnings
Registers
IP-XACT and headers, file:line
README and rationale
purpose, decisions, history
Licenses and governance
per file, per entry
Verification
simulators, self-checking, coverage
Versions
history and structural diff
cpnx_gsrd
design entry
190
registers with file and line
16
IP cores with versions
13
asynchronous clock groups
35 465
LUT baseline, Radiant 2025.1
Notes: A real entry. The numbers on the right are what the knowledge base returns today for the GSRD: 190 registers from the IP-XACT memory maps of its peripherals, each with file and line; sixteen IP cores with versions; a thirteen-group asynchronous clock plan; the Radiant 2025.1 resource usage as the baseline for any variant. Everything around the centre is a tool call away, and the spokes are where the next design's evidence pointers go.

## Slide 9
Derived by scanners, authored by people
Design with the knowledge base and arch2code
9
Derived, refreshed on every rescan
Authored, reviewed once
Structure: modules, instances, ports, parameters
Project: device, Radiant version, strategy
Constraints: clocks, false paths, I/O standards
IP: cores, versions, parameters, generated files
Flow: resources, timing, warnings per run
Verification: simulators, self-checking tests, coverage
Documentation: README sections indexed for search
Licenses: marker per file, class, copyright holder
Registers: IP-XACT memory maps and header macros
Summary, categories and tags
Design rationale in the README
Reusable-module and pattern proposals
Governance: maturity, license, provenance, export control, classification
Board facts an engineer verified (JTAG, cable, pins)
Skills: procedures for changing the design
Review answers at export: deviations, gaps accepted with reasons
+
Validation refuses a derived file that does not match a fresh scan of the pinned sources, and refuses authored content with secrets, personal data or an undeclared classification.
Notes: Two halves of every entry. The left half is produced by scanners and refreshed on every rescan; it is never typed by hand and its input hashes make a stale file a validation error. The right half is written by an engineer, through the authoring tools in a session or by hand: it is the part that carries judgement. The split is what lets derived updates merge on their own while authored content goes through review.

## Slide 10
Example: an existing design enters the base in six prompts
Design with the knowledge base and arch2code
10
The engineer says
Tool the agent calls
What is stored
1
“Look at C:\proj\cam_bridge and tell me what you need to add it to the knowledge base.”
kb_author_inspect
Nothing yet. The agent answers with the questionnaire: name, mode, top module, defines, governance values, files to leave out by license, reusable candidates.
2
“Call it cam_bridge, knowledge only, sources stay in the video repo, top is cam_bridge_top, classification internal, owner team video.”
kb_author_start
A staged entry with every derived file: structure, project, constraints, ips, flow, licenses and registers under knowledge/, plus the license audit.
3
“Summarise what it does, tag it, and mark the D-PHY deserialiser as reusable; the evidence is the lane-alignment state machine.”
kb_author_set_fields
metadata.yaml intent fields: title, summary, categories, tags, interfaces, clocks, reset, modules with reusable flag, justification and evidence.
4
“Write the Architecture and Limitations sections. Only two D-PHY lanes were tested on the board.”
kb_author_write_section
README.md sections, the limitation carrying an evidence pointer to the testbench file and line that fixes the lane count.
5
“Record how to change the number of lanes as a procedure.”
kb_author_write_skill
skills/set-lane-count/SKILL.md with When to use, Inputs, Steps, Checks and References, and skill.yaml with triggers and the files it touches; a draft until reviewed.
6
“Validate, export, and open the pull request.”
kb_author_validate
kb_author_export
kb_author_submit
The review answers (license audit accepted, two gaps accepted with reasons), reports/license_audit.md, the entry under designs/cam_bridge, branch kb/add-cam_bridge and the pull request.
Prompts 1 to 5 write only to the local authoring workspace; prompt 6 is the first that touches the repository, and it still ends in a pull request.
Notes: A worked example of the authoring path that runs entirely inside a Claude Code session. The engineer has a Radiant project for a MIPI camera bridge, cam_bridge, in the team's repository. Six prompts take it from a folder on disk to a pull request. Each prompt maps to one or two authoring tools of the knowledge-base server, and the right column says what each prompt leaves behind. Nothing touches the repository until the export in prompt six; everything before that is staged in the local authoring workspace and can be discarded.

## Slide 11
What those six prompts leave in designs/cam_bridge
Design with the knowledge base and arch2code
11
designs/cam_bridge/
metadata.yaml
name, kind, top_module, source (knowledge_only)
title, summary, categories, tags
interfaces, clocks, reset, modules.reusable
maturity, license, provenance, classification
README.md
Purpose, Architecture, Limitations, Verification
knowledge/
structure.yaml modules, instances, ports, parameters
project.yaml device, Radiant version, strategy
constraints.yaml clocks, false paths, I/O standards
ips.yaml cores, versions, parameters
flow.yaml resources, timing, warnings per run
licenses.yaml marker per file, class, holder
registers.yaml IP-XACT maps and header macros
reports/license_audit.md
skills/set-lane-count/SKILL.md, skill.yaml
prompt 2: derived by scanners
prompts 3 to 5: authored
metadata.yaml after prompt 3
summary: MIPI CSI-2 camera bridge for CertusPro-NX: 2-lane D-PHY receiver,
byte-to-pixel unpacking and an AXI4-Stream video output with line buffers
categories: [video, interface_bridge]
tags: [mipi, csi2, dphy, axi4_stream, certuspro_nx]
interfaces: [{protocol: mipi_csi2, role: receiver}, {protocol: axi4_stream, role: master}]
modules:
dphy_deser:
reusable: true
justification: lane alignment and byte-clock crossing are independent of the pixel format
evidence: [rtl/dphy_deser.sv:112]
README.md Limitations after prompt 4, SKILL.md after prompt 5
## Limitations
- Verified with two D-PHY lanes only; the four-lane configuration is
untested on hardware (evidence: tb/tb_cam_bridge.sv:41)
skills/set-lane-count/SKILL.md
## Steps
1. Set LANES in rtl/cam_bridge_top.sv:27 and the matching generic in
the Radiant project (cam_bridge.rdf)
2. Regenerate the D-PHY IP with the lane count (ips.yaml names the core)
3. Re-run the testbench; the lane-alignment check must pass for every lane
Notes: The same example seen from the repository side after the export. The folder tree on the left is what the pull request adds; the colour says which prompt produced each file. Scanners produced the whole knowledge folder from prompt two alone, and will refresh it on every rescan; the engineer's own words from prompts three to five are the metadata intent fields, the README sections and the skill. The right side shows two concrete fragments so the audience sees that what the engineer said is what the base stores, with evidence pointers rather than paraphrase.

## Slide 12
Vary the prompt, vary what is stored
Design with the knowledge base and arch2code
12
“Link it to the video repo, subpath cam_bridge”
linked
the entry points at a registered source repository and subpath; sources are fetched on demand, so the base stays small and follows the repository
“Vendor the export, but leave out the GPL files”
vendored
a copy of the sources inside the entry, with files of excluded licenses or patterns omitted and listed in the license audit
“Knowledge only, the sources stay where they are”
knowledge_only
derived facts, the engineer's words and the location of the sources; no source file enters the base
Three more things the same conversation can ask for
“That line-buffer handshake is an idiom we keep reusing; propose it as a pattern”
kb_author_propose_pattern
a pattern entry with README sections, the RTL and testbench files and exhibited_by: [cam_bridge/line_buffer]; exported only with explicit approval
“I cannot push from this machine; package it for the maintainer”
kb_author_package
one cam_bridge.kbentry.zip with checksums and the commit message; the maintainer applies it with kb_author_import_package
“Drop it, this design is not ready”
kb_author_discard
the staged entry is removed from the workspace; the repository was never touched
Notes: The first prompt decides how much of the design the base keeps. Three wordings of the same request give three source modes: a linked entry points at the team's repository and a subpath, a vendored entry copies the sources into the base with the files of unwanted licenses left out, and a knowledge-only entry keeps the derived facts and the engineer's words but no sources at all. The same session can go further: a recurring idiom becomes a pattern proposal, an engineer who cannot push packages the entry for a maintainer, and an entry that should not go in is discarded without a trace. Two things no prompt can store: secrets or personal data, which validation refuses, and files of an excluded license, which the audit lists instead.

## Slide 13
Governance and privacy: two gates, only one of them human
Design with the knowledge base and arch2code
13
maturity
license
provenance
export control
classification
C
Classification filter
public, internal, confidential; confidential entries and their sources are dropped from the distributed bundle
S
Secret and personal-data scan
keys, tokens, passwords and personal identifiers refuse validation; author lines are team identifiers
L
License audit per file
SPDX markers and copyright holders recorded; a mismatch with the declared class is a finding
Pull request from a rescan or an engineer
derived
only?
yes: knowledge and reports of existing entries, registry, inventory. Auto-merge is enabled; merges when validate, build, tests and the retrieval benchmark pass.
no: new entry, metadata, README, sources, skill, IP catalog, board, governance value. An engineer reviews and answers the governance questions.
The design gates (intent, decomposition, implementation review) approve the design, never the knowledge base.
Notes: Five governance values on every entry, with policy defaults. Three protections run on every validation. And the merge rule: a corpus pull request that changes only derived files of existing entries merges itself once CI passes; a new entry, a metadata or README change, a skill, or any governance value waits for an engineer. Confidential entries never leave the internal repository: the distributed bundle is built through a filter that drops them.

## Slide 14
The reuse ladder: the agent climbs down only with evidence
Design with the knowledge base and arch2code
14
1 Verified design
becomes the donor; its hierarchy, constraints and registers seed the decomposition
kb_find_designs, kb_get_entry, kb_get_registers
2 Reusable module
instantiated with the attribution header naming the entry and commit
kb_find_modules, kb_read_file
3 Pattern
shapes a new block; anti-patterns checked on CDC, reset, handshake
kb_find_patterns, kb_check_antipatterns
4 IP core
generated with the parameters a captured design used on this family
kb_find_ips, kb_get_ip, ipgen
5 New block
written in arch2code with hand RTL inside generated regions
design-architecture, rtl skills
Rejected candidates are listed with the reason (interface mismatch, maturity below reviewed, licence, family); a draft entry is listed but never selected.
Notes: At stage 3 the agent looks for the highest rung first. A verified design that fits becomes the donor; a reusable module is instantiated with attribution; a pattern shapes new logic; an IP core from the catalog is generated with the parameters the knowledge base recorded as known-good; a new block is written only when nothing above applies. Every step down is a rejection with a reason in decisions.md, and every value taken from an entry carries an evidence pointer.

## Slide 15
A worked trace: stage 3 of the pilot in eight tool calls
Design with the knowledge base and arch2code
15
kb_get_entry
cpnx_gsrd: RISC-V RX, AXI4, LPDDR4, TSE MAC, APB fabric, dual-boot glue
kb_get_hierarchy
axi4_to_apb_bridge_inst: the bridge the custom window hangs from
kb_get_constraints
axi_clk, cpu_clk, lpddr4 clocks from the PLL; periods not captured
kb_get_flow
LUT 35 465, FF 26 091, EBR 80, DSP 4; no timing baseline
kb_get_registers
190 registers in 5 blocks; system_gpio is the evidence source for the GPIO registers
kb_get_entry (board)
pin map, clocks, bank voltages; no JTAG or programming facts
kb_find_ips
gpio 1.8.1 and gp_timer 1.5.0 selected as register-layout references, not instantiated
kb_find_skills
no recorded procedure yet for registers, APB, timers
Found
Donor topology and the bridge to hang the window from
Resource baseline for the resource ratio
Register layouts to cite as evidence
Gaps logged for the engineer
Clock periods (read from the PLL configuration at stage 4)
Timing baseline Fmax
JTAG chain and cable of the evaluation board
Seven donor cores not installed locally
Notes: This is the real stage 3 record of the pilot design (a custom timer block in the GSRD's custom window), taken from design/decisions.md. In eight calls the agent had the donor's hierarchy, clocks, resource baseline and all 190 registers, and had chosen the catalog gpio and timer records as the register-layout reference. Equally important are the three gaps it found and logged: the clock periods, the timing baseline, and the board's JTAG facts. Those gaps are the knowledge base's to-do list.

## Slide 16
Skills: a procedure recorded once, installed everywhere
Design with the knowledge base and arch2code
16
1
Record
the engineer writes the procedure in the session (kb_author_write_skill) or by hand in the design folder
2
Review
a reviewer marks it reviewed with the review date; drafts are listed but not installed
3
Install
the bundle installer offers all, a selection or none; kb-skills manages them later
4
Reuse
kb_find_skills surfaces it at stage 3; Claude Code loads it as <design>-<skill>
What a skill looks like
designs/cpnx_gsrd/skills/add-apb-peripheral/SKILL.md
---
name: add-apb-peripheral
description: add an APB peripheral to the GSRD behind the AXI4-to-APB bridge with a new address segment and interrupt line
---
## Steps 1. kb_get_registers for the existing peripherals ... 2. propel_add_ip with the parameters of ... 3. ...
## Evidence cpnx_gsrd/soc_primary_gsrd/lib/.../component.xml:88
Notes: A design skill is a procedure for changing a captured design: add a peripheral, retarget a board, swap a memory controller. An engineer writes it once, in the session, as a SKILL.md with its steps and the evidence it relies on; after review it is installed into Claude Code by the bundle installer or on request. The next engineer asking the same question gets the procedure, not a fresh investigation.

## Slide 17
arch2code: one specification, everything else generated
Design with the knowledge base and arch2code
17
Project YAML
blocks, instances, connections,
interfaces, registers, memories,
constants and types
RTL skeletons and packages
ports, instances and wiring generated; bodies hand-written inside the regions
Register decode
APB routers and register handlers in RTL and SystemC; firmware headers with the same offsets
SystemC models and stubs
block models with channels; stubs for IP and SoC blocks generated from the ports
UVM and testbench skeletons
Config, External and Testbench scaffolds; Verilator co-simulation wrappers
Firmware headers
BASE_ADDR and REG defines from the same address map
Documentation and diagrams
block diagrams and documents from the database
Build manifest
the make flow for model, co-simulation, Questa lint and regression
Notes: arch2code is the single source of truth of a project. The YAML declares blocks, instances, connections, interfaces, registers and memories; the generator writes the RTL skeletons and packages, the register decode, the SystemC models and stubs, UVM skeletons, firmware headers and documentation, and rewrites only its own regions on every run, so hand-written code inside the files survives. A change to the specification propagates to every view at once.

## Slide 18
Simulate before you implement, then prove the registers
Design with the knowledge base and arch2code
18
1
Model simulation
generated models and stubs; run_model reports "No error" for the test the intent named
2
Co-simulation
hand-written RTL verilated in place of its model; run_cosim per block
3
Tandem verification
model and RTL side by side, transaction by transaction (Arch2Code Pro)
4
Register-access test
every declared register read after reset and written back; evidence and unverified flags honoured
What the register-access test prints (examples/regAccess, co-simulation)
regaccess uBlockA.rwUn0A[0] @0x8 reset 0x34abcdef pass
regaccess uBlockA.rwUn0A[0] @0x8 write 0x5a3c0ff0 readback pass
regaccess uBlockA.extA @0x18 write 0x5a3c0ff0 readback 0x0 unverified
regaccess uBlockB.rwUn0B @0x1000000 reset 0xabcd pass
regaccess regaccess_cpu_apbReg: 9 words, 0 mismatches
9
bus words walked
0
mismatches
1
unverified register, reported
Notes: The flow proves the intent at model level before any RTL exists: IP cores and the SoC subsystem are generated stubs whose header lists what they do not reproduce, so the first simulation runs within hours of the decomposition. Hand-written RTL is then co-simulated against the model, and tandem verification compares both. The register-access test is new: a generated bus-master thread reads every declared register after reset, writes and reads back the writable ones, and reports per register. The example in the repository runs nine words with zero mismatches, and the register declared unverified is reported, not failed.

## Slide 19
The SoC branch: one wrapper block, one custom window
Design with the knowledge base and arch2code
19
socSubsystem (arch2code wrapper block)
Propel-generated SoC top
RISC-V, interconnect, memory, peripherals
instantiated outside the generated regions
Generated stub: bus-master transactor
runs the register-access test over the window
(mdlStub: userBus: {regAccess: true})
custom window
USER_WINDOW_BASE
USER_WINDOW_SIZE
APB through the bridge
Custom logic (arch2code blocks)
customRegs router (generated)
decodes inside the window
userTimer
registers declared in YAML with evidence pointers; hand-written RTL inside generated regions; model simulated first, co-simulated after
YAML soc sections
make soc-manifest
manifest.json
propel_replay_manifest
Propel session
propel_compare_sbx_manifest
P5: the SoC is declared in the YAML, the manifest is generated, lattice-cortex replays it into Propel and compares an existing .sbx against it; the window base and size reach the firmware headers, the Propel address segment and the manifest from the same declaration.
Notes: When the intent needs a soft core, the Propel-generated SoC becomes an arch2code wrapper block: hasRtl, hasMdl and hasStub. arch2code scaffolds its RTL file and generates its ports; inside, outside the generated regions, the Propel top is instantiated. The stub is the bus-master transactor that drives the custom logic through the window before any RTL exists. The window is one pair of constants declared once in the YAML and once as the single Propel address segment. Since phase P5 the SoC itself is described in the same YAML (socProjects, socInstances, socNets, socAddresses and the other soc sections): make soc-manifest writes a manifest from it, lattice-cortex replays the manifest into a Propel session with propel_replay_manifest, as a plan or for real, and propel_compare_sbx_manifest reports where an existing SoC file deviates from it. The agent no longer builds the SoC by hand; it checks a replay.

## Slide 20
What you gain, and how it is measured
Design with the knowledge base and arch2code
20
1
Facts instead of recollection
Every value taken from the base carries a file and line; a register, a clock, a pin is cited, not remembered.
measure: entries_selected, register_evidence
2
Fewer correction loops
Known-good IP parameters, constraints and anti-pattern checks catch the mistakes before synthesis.
measure: correction_iterations, lint_clean, timing_closure
3
A restartable record
Any colleague or a later session continues from design/ without re-deriving the decisions.
measure: records_complete, rules_followed
4
Generated boilerplate, simulated early
Skeletons, decode, models, stubs and headers from one YAML; the register-access test before Gate 3.
measure: simulation_pass, reg_access_pass
Suite metric: knowledge-base lift = pass rate in kb mode minus pass rate in no_kb mode, per task tier.
Notes: Four gains, each tied to a measure the evaluation harness scores: pass rate with and without the knowledge base, correction iterations before success, context tokens per task, and workflow adherence. The harness runs every task in kb and no_kb modes, three repetitions, two models. The numbers are filled in after the first scored runs; the pilot task is defined and the rubric is in place. Until then the claim is the mechanism, not a figure.

## Slide 21
What you give back, and how little it costs
Design with the knowledge base and arch2code
21
1
Run the flow
the records under design/ are already most of the capture
2
Answer at export
sources in or out, license findings, gaps accepted with reasons, deviations, proposed patterns
3
Open the pull request
kb_author_submit opens it; a reviewer answers maturity and governance once
4
Let it refresh
linked designs rescan daily; derived updates merge on their own
D
A design
becomes a donor for the next variant
M
A module
marked reusable, instantiated with attribution
P
A pattern
an idiom that worked, or an anti-pattern to check
S
A skill
a procedure the next engineer runs instead of rediscovering
B
A board fact
the JTAG chain or pin that was missing from the entry
G
A gap
every logged gap is a request the maintainers can act on
Notes: Contribution is not a separate project. Capture is stage 13 of every design, run through the authoring tools in your own session, which the bundle installer now enables by default. The tools write only to your checkout until the pull request. The governance questions are asked once, in plain language, at export. After that, the derived half of the entry refreshes itself from the repository, and the authored half is yours to improve whenever a design touches it.

## Slide 22
Getting started in three steps
Design with the knowledge base and arch2code
22
1
Install the bundle
Unzip lattice-prompt-0.2.0-win64.zip or the Linux tarball; run install.cmd or install.sh: arch2code, cortex-kb and lattice-cortex are registered. Install the Radiant server from its own package. Native simulation needs the toolchain described in the README.
2
Open a project and state the intent
bin/new-project creates the project; make agents-setup deploys the rules and the knowledge-base skills. Say what it must do; the intake questionnaire covers the rest.
3
Finish with capture
Stage 13 runs the authoring tools; answer the export questions; the pull request is reviewed once. Your design is now the next engineer's starting point.
Where things live
Design document: Agentic FPGA System Design Architecture v1.2 (RadiantAI documents folder)
Repositories: cortex-a2c (arch2code and the skills), cortex-kb (the knowledge base), cortex-mcp (lattice-cortex), cortex-bridge (the Radiant server), lattice-prompt (the release bundle, v0.2.0)
Questions and pull-request review: the FPGA design tools team
Notes: Install the bundle: one archive, no administrator rights, the installer registers arch2code, the knowledge base and lattice-cortex with Claude Code and Claude Desktop, authoring tools on; the reviewed skills are served by the knowledge-base server and deployed per project by make agents-setup. The Radiant server comes from its own installer. Open a project folder, or an existing arch2code, Propel or captured design, and tell Claude what you want to build; the design-from-intent skill asks the intake questions. Contacts and documents are on the slide; the bundle ships a project template (bin/new-project) with the record layout.

## Slide 23
Appendix A: tool reference
Design with the knowledge base and arch2code
23
Server | Tools
cortex-kb, read-only | kb_status, kb_find_designs, kb_find_modules, kb_find_patterns, kb_find_ips, kb_find_skills, kb_find_boards, kb_get_entry, kb_get_module, kb_get_hierarchy, kb_get_dependencies, kb_find_instantiations, kb_list_files, kb_read_file, kb_get_flow, kb_get_constraints, kb_get_registers, kb_get_versions, kb_get_skill, kb_get_ip, kb_get_board, kb_check_antipatterns, kb_get_template, kb_device_notes; every reviewed skill as a prompt
cortex-kb, authoring (personal session) | kb_author_inspect, kb_author_start, kb_author_get, kb_author_set_fields, kb_author_write_section, kb_author_write_skill, kb_author_add_skill, kb_author_propose_pattern, kb_author_validate, kb_author_export, kb_author_submit, kb_author_package, kb_author_import_package, kb_author_list, kb_author_discard
arch2code | list_projects, project_info, build_db, scaffold, generate, migrate, clean, diagram, docgen, soc_manifest (P5), toolchain_detect, questa_detect, questa_compile, questa_lint, model_status, build_model, run_model, run_cosim, regression, reg_access_plan, reg_access_test, check_job, list_jobs, read_log
lattice-cortex (160 tools; the ones the flow uses) | lookup_ip, ip_search, ip_get_parameters, ip_get_ports, ip_get_memory_maps, ip_check_compatibility, find_protocol_bridge; parse_sbx, propel_session_new, propel_config_ip, propel_add_component, propel_connect_net, propel_assign_addr_seg, propel_session_validate, propel_execute; propel_replay_manifest and propel_compare_sbx_manifest (0.2.0); validate_topology, validate_build_schema (manifest-aware), validate_timing; decode_sge, firmware_plan, firmware_gen_tests, firmware_run_tests
lattice-radiant-mcp (own installer) | Radiant project and flow (prj_create, run_synthesis, run_map, run_par, run_export, run_timing), constraints lint, programming, Reveal tools; see its user guide
Notes: Reference slide for the engineers who want to see the tool names. The read-only knowledge-base tools, the authoring tools of a personal session, the arch2code server tools with the P5 manifest generator, and the lattice-cortex tools that the flow uses most, among them the two manifest tools of release 0.2.0.

## Slide 24
Appendix B: pilot status and roadmap
Design with the knowledge base and arch2code
24
P0
Environment
done: servers registered, trivial project, readiness and compatibility recorded
P1
Architecture to model
generator work done; pilot drafted to Gate 1
P2
SoC realisation
tools in place; runs after Gate 2
P3
Implementation, firmware, bring-up
tools in place; needs the board and Gate 3
P4
Capture and acceptance
task and rubric in place; scored run pending
P5
Deterministic SoC replay
tools done: soc_manifest, replay and compare (0.2.0); live replay after Gate 2
P6
Generalisation
device-agnostic design on a second family
Open items for maintainers (recorded in the pilot's decisions): merge of the cortex-mcp flow_integration branch (pull request 150), cortex-mcp README and skill refresh, the evaluation board's JTAG facts, the LSF gateway registration, the Radiant server's timing-closure packages outside the bundle.
Legend: green done, amber in progress, grey planned.
Notes: Where the programme stands today. P0 to P5 are implemented on the toolchain side and shipped in lattice-prompt 0.2.0: the manifest generator is merged in cortex-a2c, the replay and comparison tools are on the cortex-mcp flow_integration branch, which the bundle pins until the branch merges. The pilot design is drafted to Gate 1 and waits for the review; a live replay against Propel runs after Gate 2. P6 generalises to a design without a SoC on a second family.